## Slide 1
INTERCEPT® Blood System for Platelets Pathogen Reduction System
(Psoralen/UVA Treatment)
Nursing Training Module
© 2023 Cerus Corporation. Cerus, INTERCEPT and the Cerus logo are registered trademarks of Cerus Corporation. MKT-EN 00422-08 v3.0

## Slide 2
When you think of the risks associated with blood product transfusions, what
comes to mind?

## Slide 3: Do You Think About the Risk of These Viruses Being Potentially Transmitted By Transfusions?
Hepatitis C
HIV
Courtesy CDC Public Health Image Library
Courtesy CDC Public Health Image Library

## Slide 4: Do You Think About the Risk of CMV Transmission?
Platelets that are either leuko-reduced or CMV-seronegative are often referred to as “CMV-safe” or “CMV Negative” by hospital transfusion services
“CMV-safe” or “CMV Negative” units may still carry a 2.4%1 - 6.5%2 risk of CMV transmission
Bone Marrow Transplant (BMT), pediatric, and neonate patients are most susceptible to transmission of CMV
  15-20% mortality rate among BMT patients that get CMV3
  CMV pneumonia is associated with mortality rate of 80-90%3
1 . Bowden et al. Blood. 1995; 86(9):3598-3603.
2. Wu et al. Transfusion. 2010; 50:776-786.
3. Sable CA, et al. Clin Infect Dis. 1994;18:273-281.
Notes: Vamvakas EC. Transfus Med Rev 2005;19:181-99.

## Slide 5: Do You Think About the Risk of Babesia Transmission in a Transfusion?
Babesia microti, a tick-borne parasite, can cause a malaria-like illness. Although healthy children and adults with Babesiosis are often asymptomatic, the infection may be fatal in neonates, the elderly, and immune-compromised individuals
Babesia cases are observed year-round and have steadily increased over the past several years in the United States, especially in the northeast
In May 2019, FDA issued a guidance requiring year-round NAT testing for Babesia of all collections in 14 northeastern states and Washington DC or pathogen reduction for plasma or platelets collections1
FDA. Recommendations for Reducing the Risk of Transfusion-Transmitted Babesiosis: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; May 2019.

## Slide 6: Platelet Transfusions
Each year approximately 2 million platelet units are transfused to patients in the U.S.1
Many of these patient populations are compromised given their disease states (oncology, immunocompromised patient)
Platelets are transfused throughout the hospital
Chart: 
| Peds/Neonates | Transplant (Solid Organ) | Trauma/ER | ICU (Med & Surg) | Gen Medicine | Gen Surg | Cardiac Surg | Hem/Onc/BMT | All Other
 | 0.079 | 0.024 | 0.034 | 0.13 | 0.128 | 0.051 | 0.087 | 0.436 | 0.031
Free RJ et al. Transfusion. 2023;1–11.

## Slide 7: Pathway to Platelet Use: Standard Platelet Collection and Distribution
Donor
Blood Center:
Bacterial Culture
(aerobic only)
Viral Testing
12-24hr hold for results
Sent to Hospital Blood Bank
Most donations are split into 2-3 platelet units
Platelet Unit
Viruses
Bacteria
Parasites
Leukocytes
Platelet donation, like any tissue or organ donation, carries with it the host’s condition
Regardless of physical symptoms, the donor may carry any number of pathogens, for example even a healthy donor is bacteremic twice a day when they brush their teeth1
Pathogens
1. Bhanji, Pediatric dentistry 2002;24:295-9
Notes: 1. Bhanji S, Williams B, Sheller B, Elwood T, Mancl L. Transient bacteremia induced by toothbrushing a comparison of the Sonicare toothbrush with a conventional toothbrush. Pediatric dentistry 2002;24:295-9.

## Slide 8: Pathway to Platelet Use: Standard Platelet Collection and Distribution
Hospital:
Blood products are stored at the hospital blood bank
Platelets are ordered for patient use
Platelets are stored for up to 5 days at room temperature on a rocker in the blood bank
Contamination risks from viruses, emerging pathogens and parasites are largely unknown
During storage time:
Bacteria
Parasites
Remain stable in the platelet unit
Retain infectious risk
Metabolize nutrients, potentially altering pH
Rapid growth potential
Sepsis risk increases with storage time
Empty bag thrown away
Viruses
Remain stable in the platelet unit
Retain infectious risk
Leukocytes
Continue to produce cytokines
Retain transfusion-associated graft-vs-host disease risk

## Slide 9: Are Platelets Safe?
Despite implementation of interventions to mitigate bacterial contamination and reduce associated adverse events (AEs), residual risks remain…
Several recent studies demonstrate that platelets contaminated with bacteria continue to be transfused1–4
Bacterial Contamination Risk
Known/Unknown Viral and Parasite Infectious Risk
~1:1,500-2,500 Units1,6
~1:250-400 Patients5,6*
?
Zika
Yellow Fever
Babesia
Chikungunya
Dengue
Plasmodium
*Assuming 6 platelet units per patient See slide notes: 1. Dumont, 2010; 2. Pearce, 2011; 3. Murphy, 2008; 4. Walther-Wenke, 2011; 5. Kleinman, 2013; 6. Hong, 2016;
How many bacteria are safe to transfuse into your patients?
Notes: Dumont, LJ et al. Transfusion. 2010 Mar;50(3):589–99.
Pearce, S et al. Transfus Med. 2011 Feb;21(1):25–32.
Murphy, WG et al. Vox Sang. 2008 Jul;95(1)13–9.
Walther-Wenke, G et al. Vox Sang. 2011 May;100(4):359–66.
Kleinman, S et al. Transfusion. 2013 Jul;53(7):1603–18.
Hong H, et al. Blood. 2016;127(4):496-502.

## Slide 10: Why Is There A Need For Pathogen Reduced Platelets?
FDA HAS INCREASED THEIR FOCUS ON BLOOD SAFETY
Pathogen Reduction (e.g. INTERCEPT® Blood System) is an integral component of US Blood Safety Guidances:
  Bacterial risk control1
  Babesiosis risk reduction2
  Malaria risk reduction3
Transfusion Services (Hospitals) are also responsible for reducing risk of bacterial contamination in platelets
1.“Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion,” FDA Guidance for Industry, December 2020.
2. FDA. Recommendations for Reducing the Risk of Transfusion-Transmitted Babesiosis: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; 2019.
3. FDA. Recommendations to Reduce the Risk of Transfusion-Transmitted Malaria: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; 2022.
Notes: 1.“Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion,” FDA Guidance for Industry, Sept 2019.
2. FDA. Revised Recommendations for Reducing the Risk of Zika Virus Transmission by Blood and Blood Components. FDA Guidance for Industry July 2018.
3. FDA. Recommendations for Reducing the Risk of Transfusion-Transmitted Babesiosis: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; 2019.

## Slide 11: INTERCEPT® Blood System Summary FDA Approved Pathogen Reduction Technology (PRT)
*Transfusion-Associated Graft vs. Host Disease
**Data for pathogen reduction of Zika virus by the INTERCEPT Blood System, pathogen reduction system, has not been submitted for FDA review.
See slide notes: 1) FDA Guidance for Industry, December 2020; 2) AABB, 34th edition, 2024; 3) Package Insert, Cerus December 19, 2023; 4) FDA Babesiosis 2019; 5) WHO guidance 2016; 6) ECDC Zika 2017 7) FDA Zika Guidance, effective July 2018; withdrawn May 2021 after FDA determination that Zika is no longer a relevant TTI.
Industry Guidelines enable use of INTERCEPT as an option in place of certain tests and/or procedures | 
 | The FDA Guidance1 and AABB Standard 5.1.11.22 state that PRT can be used in place of bacterial testing.
 | FDA has approved and AABB Standard 5.19.4.1 allows for INTERCEPT as an alternative to gamma irradiation for the prevention of TA-GVHD*.2,3
 | INTERCEPT provides cytomegalovirus (CMV) inactivation levels3 meeting the AABB Standard 5.19.22 policy requiring methods to reduce CMV transmission risk.
 | Pathogen reduction (e.g., INTERCEPT Blood System) is an FDA recommended option to mitigate Babesia transfusion transmission for the states required to implement a strategy4 The INTERCEPT Blood System is also FDA approved to reduce the risk of T. Cruzi and Plasmodium parasite transfusion transmission.3
 | WHO5, European Centre for Disease Prevention and Control (ECDC)6 and FDA Guidance for Zika7 state that PRT** can be used in place of Zika testing or importing from non-endemic areas.
Bacteria
Emerging Pathogens
Protozoan
Parasites
CMV
T-cells
?
Notes: 1.“Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion,” FDA Guidance for Industry, Sept 2019.
2. “Standards for Blood Banks and Transfusion Services,” AABB, 31th edition, 2018.
3. The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; July 17, 2018.
4. FDA. Recommendations for Reducing the Risk of Transfusion-Transmitted Babesiosis: Guidance for Industry. In: U.S. Department of Health and Human Services FDA, ed. Silver Spring, MD: Center for Biologics Evaluation and Research; 2019.
5. “Maintaining a safe and adequate blood supply during Zika virus outbreaks. Interim guidance. WHO, February 2016.
6. “Zika Virus and Safety of Substances of Human Origin,” ECDC, July 2016.
7. FDA. Revised Recommendations for Reducing the Risk of Zika Virus Transmission by Blood and Blood Components. FDA Guidance for Industry July 2018.

## Slide 12: INTERCEPT® Blood System for Platelets Pathogen Reduction System1
There is no pathogen inactivation process that has been shown to eliminate all pathogens. Certain non-enveloped viruses (e.g., HAV, HEV, B19, and poliovirus) and Bacillus cereus spores have demonstrated resistance to the psoralen/UVA light process.
INTERCEPT
Platelet component
Patient
INTERCEPT crosslinks DNA and RNA
to prevent pathogen replication
Enveloped viruses
Non-enveloped viruses
Gram-negative bacteria
Gram-positive bacteria
Protozoa
Spirochetes
Leukocytes
Donor
Donated Platelet
UVA illumination
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; December 19, 2023.
Addition of psoralen
Notes: INTERCEPT Blood System for Platelets [Package Insert]. Concord, CA: Cerus Corporation; 2018.

## Slide 13: >4 Logs Reduction with the INTERCEPT® Blood System for Platelets1
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; December 19, 2023.
*PRV: Pseudorabies virus a model for CMV
** There is no pathogen inactivation process that has been shown to eliminate all pathogens.
b = Not tested
c = Based on culture of full platelet unit (300mL)
Viruses | Log Reduction PAS-3/Plasma
HIV-1, cell-associated | ≥5.4/≥4.7
DHBV (model virus for HBV) | ≥4.8/≥4.3
BVDV (model virus for HCV) | ≥4.1/>3.5
HTLV-I | 4.7/b
HTLV-II | ≥5.1/b
West Nile Virus | ≥6.3/>6.3
Chikungunya virus (CHIKV) | ≥5.7/>6.5
Dengue virus (DENV) | >5.4/>5.5
Cytomegalovirus (CMV), cell-associated | ≥4.9/≥4.2 (PRV*)
Influenza A virus | ≥5.9/b
Bluetongue virus | 5.2/4.4
Adenovirus | ≥4.9/≥5.3
Protozoan Parasites | Log Reduction PAS-3/Plasma
Plasmodium falciparum | ≥6.6/>6.5
Babesia microti | ≥4.9/>4.5
Trypanosoma cruzi | ≥7.8/>8.4
Bacteria | Log Reduction PAS-3/Plasma
Escherichia coli | ≥6.3/>5.9
Yersinia enterocolitica | ≥5.9/>6.3
Klebsiella pneumoniae | >6.2/>6.2
Serratia marcescens | ≥6.7c/>7.1
Staphylococcus epidermidis | ≥6.4/>6.5
Staphylococcus aureus | ≥6.6/≥6.5
Streptococcus pyogenes | ≥6.8c/>6.1
Bacillus cereus (vegetative) | ≥5.5 /≥5.6
Bacillus cereus (spore forming) | 3.7c/b
Clostridium perfringens (vegetative) | ≥6.5/>6.0
Propionibacterium acnes | ≥6.5 />6.7
Treponema pallidum | ≥6.4/>6.3
Borrelia burgdorferi | ≥6.8/>4.1
Leukocytes | Log Reduction
Human T-Cells | 4
Notes: Note that this only covers some of the pathogens inactivated by INTERCEPT

## Slide 14: What is Transfusion Associated Graft vs. Host Disease (TA-GVHD)?
  The donor leukocytes (T-cells) attack the recipient, but the recipient does not attack the donor T-Cells
  Rare but nearly always fatal
  May affect immuno-competent patients more often than thought
  Although criteria exist to determine “at risk” patients, 50% of TA-GVHD cases occur in patients who would not be predicted to be at risk for TA-GVHD by current guidelines for blood irradiation1
Kopolovic et al. A systematic review of transfusion-associated graft-versus-host disease. Blood 2015;126(3):406-414

## Slide 15: What are the Standards for T-Cell Inactivation?
The American Association of Blood Banks (AABB) standard 5.19.4 reads1:
  The blood bank or transfusion service shall have a policy regarding the prevention of transfusion-associated graft-vs-host disease (TA-GVHD)
  Methods known to prevent transfusion-associated graft-vs-host disease shall be used and include either irradiation or the use of a pathogen reduction technology that is known to inactivate residual leukocytes and is cleared or approved by the FDA or Competent Authority.
  FDA has approved and AABB Standard 5.19.4.1 allows for the INTERCEPT® Blood System to be used as an alternative to gamma irradiation for the prevention of TA-GVHD1,2
“Standards for Blood Banks and Transfusion Services,” AABB, 34th edition, 2024.
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; December 19, 2023.

## Slide 16: Reduction of T-Cells
To a level that prevents TA-GVHD1
Psoralen/UVA processed platelets exhibited a 4 log10 reduction of viable T-cells1
High number of base-pair modifications ensures inactivation of most genes
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; December 19, 2023.
Setlow, RB, et al. Irradiation of blood components. Bethesda, MD. AABB,1992 p1.
Gamma irradiation 1:37,000 strand-break: base pair
Psoralen/UVA Platelets 1:831-2 amotosalen adduct formed: base pair

## Slide 17: Reduced TTBI and No Fatalities Attributed to INTERCEPT® Platelets
 | Conventional Platelets |  | INTERCEPT Platelets | 
Year | Units Transfused (n) | TTBI (Fatalities) | Units Transfused (n) | TTBI (Fatalities)
2006-15a,b | 2,302,388 | 49 (9) | 214,293 | 0 (0)
2016b | 285,305 | 4 (0) | 21,817 | 0 (0)
2017b | 242,906 | 2 (0) | 66,004 | 0 (0)
2018b | 378 | 0 (0) | 320,235 | 0 (0)
2019b | 977 | 0 (0) | 326,605 | 0 (0)
2020b | 43 | 0 (0) | 331,149 | 0 (0)
2021b | 29 | 0 (0) | 342,641 | 1 (0)**
2005-15c,d,e | 156,809 | 13 (3) | 167,200 | 0 (0)
2016c,d | - | - | 38,374 | 0 (0)
2017c,d | - | - | 37,490 | 0 (0)
2018c,d | - | - | 38,947 | 0 (0)
2019c | - | - | 36,317 | 0 (0)
2020c | - | - | 35,715 | 0 (0)
2021c | - | - | 38,898 | 0 (0)
2009-15f | 252,809 | 9 (0) | 227,797 | 0 (0)
2016f | - | - | 65,501 | 0 (0)
2017f | - | - | 67,398 | 0 (0)
2018f | - | - | 67,395 | 1 (0)*
Total | 3,241,644 | 77 (12) | 2,443,776 | 2 (0)
* Belgium 2018: A single case of Staphylococcus hominis was reported in a patient who recovered. This case was not thoroughly investigated for modes of contamination via storage container leaks or other environmental sources.g **France 2021: Bacillus cereus transmission was reported in a patient who recovered. B. cereus is a spore-forming bacteria; the spore form is resistant to the INTERCEPT process.h |  |  |  | 
France
Cazenave, JP, et al. Pathogen Inactivation of Platelets. AABB Press: Bethesda, MD 2013; 19-176.
French National Agency for Medicine and Health Product Safety/ANSM, Hemovigilance Activity Reports, 2009–2021.
SwissMedic Haemovigilance Annual Reports, 2005–2021.
Jutzi M. et al. Transfus Med Hemother 2018;45:151-6.
Benjamin et al. Transfusion 2017;57:2946-57.
AFMPS Hémovigilance Rapport annuel: Belgium. 2016-2018.
Gammon RR, et al. Transfusion. 2022 Mar;62(3):641-650.
Lefort, C, et al Transfusion Clinique et Biologique. 2022;29:338.
Belgium
Switzerland
France

## Slide 18: INTERCEPT® Blood System for Platelets (Psoralen-Treated)
Psoralen Treatment is a proactive approach to mitigating transmission risks of platelet transfusions
Clinical summary for PSORALEN-TREATED platelets:
  Reduces the risk of transmission of a broad-spectrum of pathogensǂ known and certain emerging pathogens
  5-day shelf life
  No age or population restrictions for use1*
  An FDA guidance option to replace primary and secondary bacterial culture screening2
  FDA approved alternative to gamma irradiation for the prevention of transfusion-associated graft vs. host disease (TA-GVHD)
ǂ There is no pathogen inactivation process that has been shown to eliminate all pathogens. Certain non-enveloped viruses (e.g., HAV, HEV, B19 and poliovirus) and Bacillus cereus spores have demonstrated resistance to the INTERCEPT process.
* See warnings and contraindications slide next
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; December 19, 2023.
Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion: Guidance for Industry. US FDA; December 2020.

## Slide 19: Warnings and Contraindications for Psoralen Treated Platelets
CONTRAINDICATIONS:
Contraindicated for preparation of platelet components intended for patients with a history of hypersensitivity reaction to amotosalen or other psoralens.
Contraindicated for preparation of platelet components intended for neonatal patients treated with phototherapy devices that emit a peak energy wavelength less than 425 nm, or have a lower bound of the emission bandwidth <375 nm, due to the potential for erythema resulting from interaction between ultraviolet light and amotosalen.
WARNINGS AND PRECAUTIONS
Only INTERCEPT Processing Sets for platelets are approved for use with the INTERCEPT Blood System. Use only the INTERCEPT INT100 Illuminator for UVA illumination of amotosalen-treated platelet components. No other source of UVA light may be used. Please refer to the Operator’s Manual for the INT100 Illuminator. Discard any platelet components not exposed to the complete INT100 illumination process.
Tubing components and container ports of the INTERCEPT Blood System contain polyvinyl chloride (PVC). Di(2-ethylhexyl)phthalate (DEHP) is known to be released from PVC medical devices, and increased leaching can occur with extended storage or increased surface area contact. Blood components will be in contact with PVC for a brief period of time (approx. 15 minutes) during processing. The risks associated with DEHP released into the blood components must be weighed against the benefits of therapeutic transfusion.
Rx only. © 2024 Cerus Corporation. Cerus, INTERCEPT and the Cerus logo are registered trademarks of Cerus Corporation.
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; December 19, 2023.

## Slide 20: Hypersensitivity to Psoralens
US Package Insert
  Contraindicated for preparation of platelet components intended for patients with a history of hypersensitivity reaction to amotosalen or other psoralens.
  “Amotosalen” is the name of the specific psoralen used in the INTERCEPT Blood System treatment process
Psoralen treated products have been in routine use in patients (20+ years) with over 10 million psoralen treated components administered worldwide with no documented hypersensitivity reaction to psoralen reported to date
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; December 19, 2023.

## Slide 21: Hypersensitivity reactions to Psoralens have not been documented to date
Psoralens are present in a wide variety of foods so it is likely most people have ingested psoralens in their diet
More psoralen is consumed in one stalk of celery than used to psoralen treat one unit of platelets1
In addition, the majority of psoralen is filtered out of the platelet unit before it is sent to the hospital blood bank
FOODS RICH IN PSORALEN1 |  |  | 
Anise Seeds | Cilantro | Fennel | Lovage (Leaf Parsley)
Caraway Seeds | Coriander Seeds | Figs | Mustard Seed
Carrots | Cumin Seeds | Grapefruit | Parsnips
Celeriac | Dill | Lemons/ Limes | Root Parsley
Celery | Chevril (French Parsley) | Orange | Turnips
Wagstaff, D.J. Dietary exposure to furocoumarins. Regul. Toxico. Pharmacol. 1991;14:261-272

## Slide 22: Use with Neonatal Phototherapy
US Package Insert1
  Contraindicated for preparation of platelet components intended for neonatal patients treated with phototherapy devices that emit a peak energy wavelength less than 425 nm or have a lower bound of the emission bandwidth <375 nm, due to the potential for erythema resulting from interaction between ultraviolet light and amotosalen
American Academy of Pediatrics-Clinical Practice Guidelines2
  Recommended spectrum for intensive phototherapy: 460 – 490 nm
  Intensive phototherapy requires a narrow-spectrum LED blue light at a wavelength around 475 nm
  None of the commonly used neonatal phototherapy devices approved for market in the US today emit a peak wavelength below 425 nm, and/or a lower bound of the emission bandwidth less than 375 nm3
The INTERCEPT Blood System for Platelets Package Insert, Cerus Corporation; December 19, 2023.
Kemper et al. Clinical Practice Guideline Revision: Management of Hyperbilirubinemia in the Newborn Infant 35 or More Weeks of Gestation. Pediatrics August 2022; 150 (3): e2022058859. 10.1542/peds.2022-058859.
Bhutani et al. Phototherapy to Prevent Severe Neonatal Hyperbilirubinemia in the Newborn Infant 35 or More Weeks of Gestation. Pediatrics 2011; 128(4):e1046-1052

## Slide 23: INTERCEPT® Blood System (psoralen treated) Platelets
DIFFERENCES IN PLATELET BAG APPEARANCE
    Bag is 2.8 inches longer, however the platelet volume is the same
    No IRRADIATION Sticker
    INTERCEPT BLOOD SYSTEM embossed across the top of the bag
CONVENTIONAL PLATELET
PSORALEN TREATED
PLATELET

## Slide 24: Administration of INTERCEPT® Blood System (psoralen-treated) Platelets
Platelet dosing and volume of the psoralen-treated platelets are the same as conventional platelet products.
Pre-medication and hang time for psoralen-treated platelets are the same as conventional platelet products.
Patients may receive both conventional platelets and psoralen-treated platelets to fill their transfusion requirements.
Psoralen-treated platelets can be transfused in the same line as conventional platelets.

## Slide 25: INTERCEPT® Blood System (Psoralen Treated) Platelet Labeling
    Labeled as: APHERESIS PLATELETS (PAS-C ADDED) LEUKOCYTE REDUCED
      PAS-C is the solution that the platelets are collected in at the time of donation, if not in plasma
    Note new wording added to label: PSORALEN TREATED
APHERESIS PLATELETS
PAS-C ADDED LEUKOCYTES REDUCED PSORALEN-TREATED
APHERESIS PLATELETS LEUKOCYTES REDUCED PSORALEN-TREATED

## Slide 26: IRRADIATED VS. PSORALEN TREATED Platelet Labeling
An INTERCEPT treated (psoralen treated) platelet unit may be administered when an irradiated platelet unit is ordered.
Psoralen treatment is an FDA approved alternative to gamma irradiation for the prevention of Transfusion Associated Graft vs. Host Disease (TA-GVHD)
NO Rad-SureTM sticker will be present on the psoralen treated platelets
An auxiliary sticker or tie tag as pictured (yellow) may be added to a psoralen treated platelet
PSORALEN TREATMENT of platelets is an FDA approved alternative to GAMMA IRRADIATION of platelets.

